Analysis results of the 2004 CMS testbeam data

Authors: Cristina Fernández and Pablo Aguayo

Date: 01/25/2005

CIEMAT

The cases studied follow the  “ROB problems” described in the document:

http://wwwae.ciemat.es/cms/talks/cmsweek_dec04/TB_ROBproblems.pdf written by M. C. Fouz.

- Case 1: Strange 1st. Event number

- Case 2: Empty ROB. Two “Type15” chains, do not consider disconnected ROB (ROS1-ROB3/ROB7 and ROS2-ROB7)

- Case 3: Multi Event. Within the same DAQ event there are two or more ROB header-trailer (Type0-Type1)

- Case 4: TDC Master. Different TDC Master in the same ROB in header and trailer.

- Case 5: Bunch Diffs. Different Bunch Counter of any ROB in the same event.

- Case 6: Event Diffs. When the DAQ Event number and the ROB Event number have a difference larger than 1.

- Case 7: WC Diffs.  Different “Word Count” received and observed in the ROB trailer.

| File name | Events | 1st. Event | Empty ROB | Multi Event | TDC Master | Bunch diffs. | Event diffs. | Wc diffs. | Error type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 041003_run_2082 | 10001 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Type: 0 detected |
| auto_41_delay_0_2379 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| auto_41_delay_10_2389 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_11_2390 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_12_2391 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_1_2380 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_13_2392 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_14_2393 | 28570 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_15_2394 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_16_2395 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_17_2396 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_18_2397 | 24677 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_19_2398 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_20_2399 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_21_2400 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_22_2401 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_2_2381 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_23_2402 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_24_2403 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_3_2382 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_4_2383 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_5_2384 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_6_2385 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_7_2386 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_8_2387 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_41_delay_9_2388 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_0_2348 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| auto_42_delay_10_2358 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_11_2359 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_12_2360 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_1_2349 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_13_2361 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_14_2362 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_15_2363 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_16_2364 | 28343 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_17_2365 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_18_2366 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_19_2373 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_20_2367 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_20_2374 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_21_2368 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_21_2375 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_22_2369 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_22_2376 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_2_2350 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_23_2370 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_23_2371 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_23_2377 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_23_2378 | 21508 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_24_2372 | 28835 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_3_2351 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_4_2352 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_5_2353 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_6_2354 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_7_2355 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_8_2356 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_42_delay_9_2357 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_0_2318 | 10000 | 1 | 0 | 11 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_0_2322 | 1004 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_0_2323 | 20000 | 1005 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_10_2333 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_11_2334 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_12_2335 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_1_2319 | 10834 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_1_2324 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_13_2336 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_14_2337 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_15_2338 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_16_2339 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_17_2340 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_18_2341 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_19_2342 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_20_2343 | 22118 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_21_2344 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_22_2345 | 25519 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_2_2320 | 10000 | 10835 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_2_2325 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_23_2346 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_24_2347 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_3_2326 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_4_2327 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_5_2328 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_6_2329 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_7_2330 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_8_2331 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| auto_43_delay_9_2332 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| bt_43_delay_2_2321 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| bt_default_syncro02_2405 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| bt_default_syncro03_2406 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| bt_default_syncro03_2407 | 11487 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| bt_default_syncro_2404 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2165 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2166 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2167 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2168 | 1000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| pusync_2169 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2170 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2171 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2188 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2189 | 200 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| pusync_2190 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2191 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2192 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2193 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2194 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2195 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2196 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2197 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2198 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2199 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2200 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2201 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2202 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2203 | 200 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| pusync_2204 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2205 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2206 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2207 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2208 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2209 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2210 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2211 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2212 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2213 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2214 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2215 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2216 | 387 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2217 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2218 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2219 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2220 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2221 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2222 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2223 | 200 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| pusync_2224 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2225 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| pusync_2226 | 200 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2133 | 1098 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2146 | 1705 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2150 | 1000 | 4593 | 0 | 0 | 0 | 0 | 0 | 1000 | Error Type: 6 detected |
| run_2153 | 1000 | 5134 | 0 | 0 | 0 | 0 | 0 | 1000 | Error Type: 6 detected |
| run_2156 | 10000 | 27726 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2158 | 10886 | 91325 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2159 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2161 | 5000 | 35703 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2162 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2440 | 1000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2441 | 1000 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| run_2442 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2443 | 1000 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |
| run_2480 | 500 | 3405 | 7 | 0 | 0 | 0 | 0 | 0 | Type 14: nonsense ROS number |
| run_2481 | 500 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2482 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2483 | 2659 | 1 | 169 | 222 | 13 | 4407 | 0 | 31 | (Error Type: 6 and 7 detected) Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2484 | 500 | 2660 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2485 | 690 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2486 | 55 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2488 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2490 | 44 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2491 | 10000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2492 | 5307 | 1 | 0 | 0 | 0 | 6138 | 0 | 0 |  |
| run_2493 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2494 | 356 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2495 | 89 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2496 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2497 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2498 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2499 | 10025 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2500 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2501 | 1000 | 1 | 1 | 7 | 0 | 6 | 0 | 0 |  |
| run_2502 | 1767 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2503 | 1000 | 1768 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2504 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2505 | 2449 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2506 | 1000 | 2450 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2507 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2508 | 2459 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2509 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2510 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2511 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2512 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2513 | 579 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2514 | 1000 | 580 | 1 | 0 | 0 | 0 | 0 | 0 |  |
| run_2515 | 304 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2516 | 1000 | 305 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2517 | 2066 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2518 | 10988 | 2067 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2519 | 100034 | 10989 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2520 | 418 | 100035 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2521 | 100269 | 419 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2522 | 1000 | 100270 | 7 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2523 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2524 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2525 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2526 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2527 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2528 | 1713 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2529 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2530 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2540 | 3141 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2541 | 8635 | 3142 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2542 | 3850 | 8636 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2543 | 0 | 8636 | 0 | 0 | 0 | 0 | 0 | 0 | (Without data) |
| run_2544 | 0 | 8636 | 0 | 0 | 0 | 0 | 0 | 0 | (Without data) |
| run_2545 | 0 | 8636 | 0 | 0 | 0 | 0 | 0 | 0 | (Without data) |
| run_2546 | 3162 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2547 | 2197 | 3163 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2548 | 1274 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2549 | 869 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2550 | 21876 | 870 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2551 | 33918 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2552 | 34912 | 33919 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2553 | 33412 | 34913 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2554 | 50229 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2555 | 50000 | 50230 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2556 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2557 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2558 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2559 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2560 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2561 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2562 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2563 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2564 | 50425 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2565 | 50000 | 50426 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2566 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2567 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2568 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2569 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2570 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2571 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2572 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2573 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2574 | 59850 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2575 | 59119 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2576 | 35139 | 59120 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2577 | 1000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2578 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2579 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2580 | 1017 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2581 | 1000 | 1018 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2582 | 6364 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2583 | 1000 | 6365 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2585 | 1000 | 44915 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2586 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2588 | 4498 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2589 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2590 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2591 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2592 | 4160 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2593 | 5151 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2594 | 2937 | 5152 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2595 | 5987 | 2937 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2596 | 1924 | 5988 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2597 | 42314 | 1925 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2598 | 40430 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2599 | 50000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2600 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2601 | 50421 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2602 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2603 | 100000 | 1 | 1 | 6 | 0 | 6 | 0 | 0 |  |
| run_2604 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2605 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2606 | 113996 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2607 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2608 | 75000 | 1 | 1 | 10 | 0 | 0 | 0 | 0 |  |
| run_2609 | 6457 | 1 | 0 | 11 | 0 | 0 | 0 | 0 |  |
| run_2610 | 75000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2611 | 75000 | 1 | 1 | 7 | 0 | 6 | 0 | 0 |  |
| run_2612 | 10000 | 1 | 1 | 11 | 0 | 6 | 0 | 0 |  |
| run_2613 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2614 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2615 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2616 | 10000 | 1 | 0 | 8 | 0 | 0 | 0 | 0 |  |
| run_2617 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2618 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2619 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2620 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2621 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2622 | 10000 | 1 | 0 | 11 | 0 | 6 | 0 | 0 |  |
| run_2623 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2624 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| run_2625 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2626 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2627 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2628 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2629 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2630 | 10000 | 1 | 0 | 6 | 2 | 0 | 1 | 12 |  |
| run_2631 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2632 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2633 | 10000 | 1 | 0 | 12 | 0 | 6 | 0 | 0 |  |
| run_2634 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2635 | 10000 | 1 | 0 | 11 | 0 | 6 | 0 | 0 |  |
| run_2636 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2637 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2638 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2639 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2640 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2641 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2642 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2643 | 21896 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2644 | 20000 | 1 | 0 | 10 | 0 | 0 | 0 | 0 |  |
| run_2645 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2646 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2647 | 20000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| run_2648 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2649 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2650 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2651 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2652 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2653 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2654 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2655 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2656 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2657 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2658 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2659 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2660 | 20000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| run_2661 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2662 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2663 | 20000 | 1 | 0 | 11 | 0 | 6 | 0 | 0 |  |
| run_2664 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2665 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2666 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2667 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2668 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2669 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2670 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2671 | 20000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2672 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2673 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2674 | 22901 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2675 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2676 | 20000 | 1 | 0 | 8 | 0 | 6 | 0 | 0 |  |
| run_2677 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2678 | 20000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| run_2679 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2680 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2681 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2682 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2683 | 20000 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock ED vs PowerUp: 77 |
| run_2684 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2685 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2686 | 20000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2687 | 21688 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2688 | 23027 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2689 | 20000 | 1 | 3 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock B9 vs PowerUp: 77 |
| run_2690 | 20000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 23 vs PowerUp: 1D |
| run_2691 | 20000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2692 | 922 | 1 | 7 | 11 | 0 | 6 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2693 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2694 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2695 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2696 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2697 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2698 | 36353 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2699 | 65000 | 1 | 0 | 21 | 0 | 12 | 11 | 0 |  |
| run_2700 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2701 | 53829 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2702 | 20000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2703 | 20000 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| run_2704 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2705 | 20339 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2706 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2707 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2708 | 20000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| run_2709 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2710 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2711 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2712 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2713 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2714 | 20000 | 1 | 0 | 11 | 0 | 0 | 0 | 0 |  |
| run_2715 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2716 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2717 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2718 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2719 | 25173 | 1 | 0 | 10 | 0 | 0 | 0 | 0 |  |
| run_2720 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2721 | 30903 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2722 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2723 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2724 | 20000 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| run_2725 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2726 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2727 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2728 | 2000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2729 | 50000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2730 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2731 | 57796 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2732 | 55703 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2733 | 55034 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2734 | 55882 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2735 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| run_2736 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2737 | 50017 | 1 | 1 | 10 | 0 | 0 | 0 | 0 |  |
| run_2738 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2739 | 100000 | 1 | 1 | 11 | 0 | 0 | 0 | 0 |  |
| run_2740 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2741 | 100000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2742 | 10000 | 1 | 1 | 8 | 0 | 6 | 0 | 0 |  |
| run_2743 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2744 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| run_2745 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2746 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2747 | 10000 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| run_2748 | 10000 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| run_2749 | 10000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| run_2750 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2751 | 10000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2752 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2753 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2754 | 10000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| run_2755 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2756 | 10000 | 1 | 0 | 11 | 0 | 6 | 0 | 0 |  |
| run_2757 | 10000 | 1 | 0 | 21 | 0 | 6 | 2 | 0 |  |
| run_2758 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2759 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2760 | 11460 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2761 | 10000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2762 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2763 | 10000 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| run_2764 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2765 | 10000 | 1 | 3 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 6D vs PowerUp: 3B |
| run_2766 | 10000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2767 | 10000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| run_2768 | 10000 | 1 | 3 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 6D vs PowerUp: 3B |
| run_2769 | 10000 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| run_2770 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| run_2771 | 10000 | 1 | 0 | 8 | 0 | 0 | 0 | 0 |  |
| run_2772 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2773 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2774 | 10000 | 1 | 1 | 10 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 89 vs PowerUp: 77 Datos en ROS2 ROB7 ???? |
| run_2775 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2776 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2777 | 10000 | 1 | 0 | 10 | 0 | 0 | 0 | 0 |  |
| run_2778 | 20000 | 1 | 1 | 12 | 0 | 0 | 0 | 0 |  |
| run_2779 | 23111 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2780 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2781 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2782 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2783 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2784 | 20000 | 1 | 0 | 12 | 0 | 6 | 0 | 0 |  |
| run_2785 | 20000 | 1 | 0 | 9 | 0 | 0 | 0 | 0 |  |
| run_2786 | 20000 | 1 | 0 | 12 | 0 | 6 | 0 | 0 |  |
| run_2787 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2788 | 27011 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2789 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2790 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2791 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2792 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2793 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2794 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2795 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2796 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2797 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2798 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2799 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2800 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2801 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| run_2802 | 20000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_0_run_2256 | 10000 | 1 | 7 | 10 | 0 | 6 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_15deg_41_10_run_2266 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_11_run_2267 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_12_run_2268 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_13_run_2269 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_14_run_2270 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_15_run_2271 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_16_run_2272 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_17_run_2273 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_18_run_2274 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_19_run_2275 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_1_run_2257 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_20_run_2276 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_21_run_2277 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_22_run_2278 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_23_run_2279 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_24_run_2280 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_2_run_2258 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_3_run_2259 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_4_run_2260 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_5_run_2261 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_6_run_2262 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_7_run_2263 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_8_run_2264 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_41_9_run_2265 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_0_run_2228 | 10000 | 1 | 8 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_15deg_42_0_run_2229 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_10_run_2239 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_11_run_2240 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_12_run_2241 | 10936 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_13_run_2242 | 10000 | 10937 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_14_run_2244 | 11633 | 1113 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_15_run_2245 | 10000 | 11634 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_16_run_2246 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_17_run_2247 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_18_run_2248 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_19_run_2249 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_1_run_2230 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_20_run_2250 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_21_run_2251 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_22_run_2252 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_23_run_2253 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_24_run_2254 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_2_run_2231 | 11183 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_3_run_2232 | 10000 | 11184 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_4_run_2233 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_5_run_2234 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_6_run_2235 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_7_run_2236 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_8_run_2237 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_15deg_42_9_run_2238 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_0__2444 | 20000 | 1 | 7 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_0__2449 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_10__2459 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_11__2460 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_12__2461 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_1__2445 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_1__2450 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_13__2462 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_13_test_2463 | 1000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_14__2464 | 225 | 1 | 3 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 6D vs PowerUp: 3B |
| syncro_at_0deg_42_14__2465 | 20000 | 226 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_15__2466 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_16__2467 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_16__2468 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_17__2469 | 20000 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock AF vs PowerUp: 77 |
| syncro_at_0deg_42_18__2470 | 20000 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 45 vs PowerUp: 3B |
| syncro_at_0deg_42_19__2471 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_20__2472 | 20000 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 45 vs PowerUp: 3B |
| syncro_at_0deg_42_21__2473 | 20000 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 45 vs PowerUp: 3B |
| syncro_at_0deg_42_22__2474 | 20000 | 1 | 3 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock B9 vs PowerUp: 77 |
| syncro_at_0deg_42_2__2446 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_2__2451 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_23__2475 | 20000 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock 45 vs PowerUp: 3B |
| syncro_at_0deg_42_24__2476 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_at_0deg_42_24__2478 | 576 | 11316 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_3__2447 | 2000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_3__2448 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_3__2452 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_4__2453 | 20000 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock AF vs PowerUp: 77 |
| syncro_at_0deg_42_5__2454 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_6__2455 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_7__2456 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_8__2457 | 20000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_at_0deg_42_9__2458 | 20000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_0deg_42_0_2408 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_10_2418 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_11_2419 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_11__2421 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_12__2422 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_1_2409 | 10000 | 1 | 0 | 11 | 0 | 6 | 0 | 0 |  |
| syncro_bt_0deg_42_13__2423 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_14__2424 | 11153 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_15__2425 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_16__2426 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_17__2427 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_18__2428 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_19__2429 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_20__2430 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_20__2431 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_21__2432 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_22__2434 | 10000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_0deg_42_2_2410 | 11709 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_23__2435 | 10000 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock AF vs PowerUp: 77 |
| syncro_bt_0deg_42_23__2437 | 10000 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock AF vs PowerUp: 77 |
| syncro_bt_0deg_42_24__2436 | 10000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_0deg_42_24__2438 | 10000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_0deg_42_3_2411 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_4_2412 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_5_2413 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_6_2414 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| syncro_bt_0deg_42_7_2415 | 10722 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_8_2416 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_0deg_42_9_2417 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_0_run_2281 | 10000 | 1 | 7 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_15deg_42_0_run_2288 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_10_run_2292 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_11_run_2293 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_12_run_2294 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_13_run_2295 | 10000 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_14_run_2296 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_15_run_2297 | 10000 | 1 | 0 | 11 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_16_run_2298 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_17_run_2299 | 10000 | 1 | 0 | 12 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_18_run_2300 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_19_run_2301 | 10000 | 1 | 0 | 9 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_1_run_2282 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_20_run_2302 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_21_run_2303 | 10000 | 1 | 0 | 7 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_22_run_2304 | 462 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_22_run_2305 | 10000 | 463 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_23_run_2306 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_24_run_2307 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_24_run_2308 | 10000 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_24_run_2309 | 10000 | 1 | 6 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_15deg_42_24_run_2311 | 10000 | 1 | 0 | 7 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_24_run_2312 | 14562 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_15deg_42_24_run_2313 | 10000 | 1 | 6 | 12 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_15deg_42_24_run_2314 | 10000 | 1 | 7 | 0 | 0 | 0 | 0 | 0 | Type 14: ROS1:Lock FF vs PowerUp: 77 |
| syncro_bt_15deg_42_2_run_2283 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_3_run_2284 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_4_run_2285 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_5_run_2286 | 10000 | 1 | 0 | 11 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_6_run_2287 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_7_run_2289 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_bt_15deg_42_8_run_2290 | 10000 | 1 | 0 | 10 | 0 | 6 | 0 | 0 |  |
| syncro_bt_15deg_42_9_run_2291 | 10000 | 1 | 0 | 12 | 0 | 0 | 0 | 0 |  |
| syncro_TP_15deg_42_0_run_2255 | 2001 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |