OFCu-RO

Documentation

Version 0.6 (2013-09-18)

Build number: 1

1.	Functional description	2

2.	Hardware description	3

2.1	Mechanical board specifications	3

2.2	Power distribution system	3

2.3	Clock	3

2.4	FPGA	3

2.5	Optical to electrical data path	3

2.6	Front panel	4

2.7	Rear connections	4

J2	4

TIMbus	4

3.	Software description	6

3.1	Slow control interface	6

Signals	6

Communication protocol	6

Register description	6

3.2	One-wire lines operation	8

3.3	Optical modules control and monitoring	9

3.4	TSC link	9

Overview	9

OFCu-RO specific information	9

3.5	LED indicators	10

# Functional description

The OFCu-RO performs the following functions:

- Converts the 25 arriving readout data links to differential signals. 24 channels are converted by two different 12-fibre receiver modules from AVAGO (AFBR-742BZ) and the 25th by a FTLF8519F2KCL transceiver. The electrical signals are passed through seven 4-channel DS90LV804 LVDS buffers and AC-coupled to the RJ-45 connectors that route them to the front panel of the ROS boards.

- Receives an optical serial data link from a similar board situated back-to-back of the TSC board, deserializes it, processes the communication overhead bits to check for integrity and other potential problems, and delivers the information, when requested, to the ROS board through the backplane pass-through connector, emulating the behaviour of the TSC board. The optical module used for transduction is a Finisar FTLF8519F2KCL.

- Communicates through the J2 backplane with the VME_patch board, which, in term, can be accessed by means of the VMEbus to which it is connected. The communication is mainly register-based with 4-bits address bus and 8-bits data bus, although the signal-detect signals for the three OFCu modules are passed directly through the backplane.

# Hardware description

## Mechanical board specifications

The dimensions of the board comply with the VME standard specifications for a Rear Transition Module (see IEEE 1101.1 & IEEE 1101.11). The VME connectors used are compliant with IEC 60603-2 (DIN 41612), and the backplane pass-through pins are 13.2 mm long (instead of the more-common 17 mm)

Vertical dimension is 6U (233.35 mm) and board depth is 160 mm (163.8 mm, in fact, to account for the shorter pins of the pass-through connectors).

## Dual PCB layout

Given the similarities between the OFCu-RO and the TSC_rear functionality and design, a PCB has designed that can serve for both boards, depending on the components mounted

## Power distribution system

- Input voltage is 5V, arriving through both J2 and J3 connectors and then passed through a fuse. 3.3 V and 1.2 V are needed for operation, and are obtained in cascade.

- Both bias voltages are obtained in the same way: an LTC4361CTS8-2#TRMPBF overvoltage/overcurrent protection controller drives a NFET that interrupts supply in case of failure. A linear regulator (mic29301-3.3V and MCP1824-1202E/OT) converts the voltage levels, and power is stabilized by means of bypass capacitors both close to the regulators and to each individual IC. Voltage and current is additionally measured by a DS2438Z 1-wire intelligent battery monitor.

- All four optical modules have individual inductive-resistive-capacitive power filtering networks as recommended on the manufacturer's datasheet.

- Several bypass capacitors are placed close to the FPGA, as recommended by manufacturer.

## Clock

40 MHz LHC clock is received through the TIMbus connector. When the absence of external clock is detected by SN74LVC1G123-DCT, a local clock generated by a crystal oscillator is routed to the FPGA and a flag is activated.

## FPGA

- A Xilinx XC6SLX4-2TQG144C Spartan-6 FPGA does all the data processing and interface communication needed.

- The FPGA FW can be loaded directly from a XCF04SVOG20C flash memory automatically on power-on, and on demand by pressing U7 button.

- The FPGA and the flash memory can be written by using a standard JTAG connector and interface.

- There are 6 user-programmable LEDs (of which 4 can be seen from the front panel) and several single-ended and differential signals for testing and for future additional functionality.

## Optical to electrical data path

- The optical links from UXC are received by two AVAGO (AFBR-742BZ) and a Finisar FTLF8519F2KCL modules (the finisar needs DC restoration). The electrical signal is buffered (DS90LV804), AC-coupled (100 nF) and output to RJ-45 connectors. There is a series short-circuited resistor footprints to allow for hypothetical future modifications in the adaptation network.

- The control signals are controlled from the FPGA and pulled to a default level in case they are left undriven.

- The signal-detect signals are routed both to the FPGA and directly to the VME_patch through the J2 connector

- An additional finisar FTLF8519F2KCL receives the optical data link from the TSC_rear board and sends it to the FPGA. The SD in this case is only routed to the FPGA.

## Front panel

- 2 MTP sockets corresponding to the AVAGO receiver modules

- 4 LC sockets corresponding to the two Finisar transceiver modules

- 4 hard-wired LED indicators:

  - 3.3 V: continuous green if power ok.

  - 1.2 V: continuous green if power ok.

  - CLK: yellow if working with local clock (remote clock unavailable).

  - DONE: FPGA loading ok

- 4 programmable LED indicators; its behaviour is described in detail later.

- 8 RJ-45 sockets

## Rear connections

### J2

- Three signal detect outputs: pulled down and then buffered

- Board_sel input: pulled down and negated; controls the enable of the following buffer ICs that interface to lines in the J2 connector:

  - SN74LVCH16244ADGGR (tri-state buffer of OFCu inputs):

    - reset (pulled down before and after the buffer)

    - 4 address bits

    - write_reg bit (pulled down after the buffer)

    - 3 spare lines (read_reg, spare0 and spare1)

  - SN74LVT16245ADGGR: direction is controlled by the write_reg bit, buffers all 8 data bits.

  - SN74LVT16245ADGGR: direction is controlled by FPGA, buffers 3 spare lines (spare2-4)

- Individual spare line: buffered individual spare line whose direction can be selected by soldering appropriate short circuits in two empty 0602 footprints.

### TIMbus

- Input differential to single-ended buffer for ROS-Ready signal (terminated and dc-restored).

- Input differential to single-ended buffer for L1A signal

- Input differential to single-ended buffer for EVCNTRES1A signal

- Input differential to single-ended buffer for CKDES2 signal (clock)

- Output single-ended to differential buffer for TRG_STROBE signal

- Bidirectional single-ended to differential buffer (SN65LVDM1676) for TRG_DATA(0-15) bus. Input/output behaviour controlled by FPGA, hard-coded in FW to output.

## Other relevant PCB components

- The 20-pin P7 connector has lines routed to the FPGA that can be used for FW debugging.

- The 14-pin P1 connector serves for JTAG programming of the FPGA and flash memory.

- The U7 pushbutton triggers a re-programming of the FPGA from the flash memory.

- Jumpers P2-P7 are connected to ground

- LEDs D8 and D9 are controlled by the FPGA

# Software description

## Slow control interface

### Signals

- Board select (bsel): enables the appropriate buffers so that only one of the boards makes use of the shared bus, and informs the FPGA that it is being adressed.

- Write (wr): determines the type of communication (write register or read register)

- Reset: reset signal to the FPGA

- Address bus (add)(4): selects the register to operate on (0-15)

- Data bus (data)(8): data byte to write or to be read

### Communication protocol

VME_patch point of view

- The VME_patch drives the WR and ADD(3-0) signals, and optionally, DATA(7-0) if WR=1

- Wait time = XXX ns to avoid racing condition

- The VME_patch drives the corresponding BSEL line

- Wait time = XXX ns to ensure the OFCu has time to update the register (WR=1) or to drive the data bus (WR=0)

- Data bus is read (WR=0 only) and all lines are freed by VME_patch (both cases)

- Wait time = XXX ns to ensure the OFCu has time to end the register access cycle.

OFCu point of view

- when BSEL is detected:

  - (WR=1) ( reads data bus and updates the contents of register determined by ADD(3-0)

  - (WR=0) ( drives the data bus with the contents of register determined by ADD(3-0)

- when BSEL is released, the cycle ends and data bus is released

### Register description

Each register is identified by its ordinal, the hexadecimal offset, the FW name, and whether it is writable or read-only.

The standard addressing space covers registers 0-15 (0x00 – 0x1E). Registers above those are accessed via a store – recall procedure that uses registers 0 and 1 (0x00 and 0x02). Writing in register #1 moregs_ctrl (0x02) triggers a recall (if msb = 0) or store (if msb = 1) operation on the register identified by the address contained in moregs bits 6 downto 0 (128 registers maximum addressing space). The registers contents are copied from register #0 moregs_data (0x00) to the corresponding register in a store operation, from the corresponding register to moregs_data register in the recall operation.

0 (0x00) – moregs_data (w/r)

Data to be stored to (or recalled from) one of the registers in the extended register addressing space, triggererd by the corresponding wrirte operation on register #1.

1 (0x02) – moregs_ctrl (w/r)

| store/ _recall | A | D | D | R | E | S | S |
| --- | --- | --- | --- | --- | --- | --- | --- |

2 (0x04) - ow1_ctrl_reg (w/r)

1-wire line (1.2 V monitoring) commands

| -- | -- | -- | read 8b | write 8b | read 1b | write 1b | init |
| --- | --- | --- | --- | --- | --- | --- | --- |

3 (0x06) – ow1_data_reg (w/r)

1-wire line (1.2 V monitoring) data byte (msb for 1-bit read operations, lsb for 1-bit write operations)

4 (0x08) - ow1_crc_reg (r/o)

1-wire line (1.2 V monitoring) CRC byte

5 (0x0A) - ow3_ctrl_reg (w/r)

same as register 2, for 3.3 V monitoring, plus:

when a WR command is done in this register with the most significant bit active, the three most significant bits of this register are internally rewritten to identify the type of build loaded to the configuration PROM (the validation build is described later):

bit 6: “1” operation, “0” validation

bit 5: “1” OFCu-ROS, “0” TSC-rear

6 (0x0C) - ow3_data_reg (w/r)

same as register 3, for 3.3 V monitoring

7 (0x0E) - ow3_crc_reg (r/o)

same as register 4, for 3.3 V monitoring

8 (0x10) - sd_status_reg (r/o)

Signal detect status register. The 4 LSB are real time values, the 4 MSB are latched on loss of signal. WR command on this register resets latches regardless of data written.

| sd_ch24 | sd_tsc | sd_avago2 | sd_avago1 | sd_ch24 | sd_tsc | sd_avago2 | sd_avago1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (latched value) | (live value) |

9 (0x12) - opto_ctrl_reg (w/r)

Avago modules' control signals (receiver enable, squelch enable, enable SD).

| tx2_dis | tx1_dis | rx_en2 | rx_en1 | sq_en2 | sq_en1 | en_sd2 | en_sd1 |
| --- | --- | --- | --- | --- | --- | --- | --- |

Default value = 11111111 (this is the only register in which the default value is different in OFCu-RO/TSC_rear boards, so it also serves for board identification)

10 (0x14) – tsc_status_0_la (r/o)

11 (0x16) – tsc_status_1_la (r/o)

12 (0x18) – tsc_status_2_la (r/o)

These three registers can be concatenated into a 24-bit word that contains several error flags for the tsc link status.

The flags are as follows (0 being the lsb, that is, the lsb of register #10):

| # | Flag name | Short description |
| --- | --- | --- |
| 0 | err_bufpll | Bufpll not locked |
| 1 | err_pll | Pll not locked |
| 2 | err_stayatlimit | Iodelay hit range end |
| 3 | err_ixo_lcl | No external clock, working with local |
| 4 | err_lock | Lost lock to data stream |
| 5 | err_ecr_rmt | ECR word received through serial link but no ECR on TTC first |
| 6 | err_ecr_lcl | ECR received through TTC but not through serial link |
| 7 | err_fifo | Fifo full |
| 8 | err_ros_rdy | L1A received but ros_ready not asserted |
| 9 | err_ros_rdy_fast | Ros_ready deasserted before communication ended |
| 10 | err_ros_rdy_held | Ros_ready not deasserted alter comunication ended |
| 11 | err_hdr_ali | Header’s event counter different than expected |
| 12 | err_hdr_bad | Non-header word received when expecting a header |
| 13 | err_hdr_wait | No header word received |
| 14 | err_dat_wait | No data received alter header |
| 15 | err_dat_sudden_end | Idle word received befote trailer |
| 16 | err_dat_count_match | Counted data words different from trailer value |
| 17 | err_dat_count_max | Maximum data words limit reached |
| 18 | err_bad_data_trail | Non-data and non-trailer word received |

Although these registers are read only, a write command can be issued. Instead of changing the registers’ content, it has the following consequences:

- tsc_status_0_la: simulate successful ECR (same as a real ECR but no ECR word is expected from the serial link)

- tsc_status_1_la: clear latch for all three tsc_status registers

- tsc_status_2_la: resets input deserializer

13 (0x1A) – test0_reg  (r/o)

14 (0x1C) – test1_reg (r/o)

15 (0x1E) – test2_reg (r/o)

16 (0x20) – tsc_maxwords (r/w)

Maximum event size from the tsc_rear that will be passed to the ROS.

Default value = 80.

18 (0x24) – tsc_ecrwait (r/w)

Maximum number of clock cycles (BX’s) that can be waited from the reception of an ECR signal until the ecr word is received on the tsc serial link.

Default value = 50.

19 (0x26) – tsc_roswait1 (r/w)

Maximum number of clock cycles (BX’s) that can be waited between the time at which the ofcu_ros has finished processing an event and a new L1A is received, and the rising edge of the signal ros_ready. The contents of this register are multiplied by 64.

Default value = 100 (equivalent to 6400 BX’s).

20 (0x28) – tsc_headerwait (r/w)

Maximum number of clock cycles (BX’s) that can be waited from the assertion of the ros_ready signal until a header word for that event is received on the tsc serial link.

Default value = 50.

21 (0x2A) – tsc_datawait (r/w)

Maximum number of clock cycles (BX’s) that can be waited from the reception of the header word to the first data word on the tsc serial link.

Default value = 50.

22 (0x2C) – tsc_roswait2 (r/w)

Maximum number of clock cycles (BX’s) that can be waited from the de-assertion of the trg_strobe signal until the ROS de-asserts the ros_ready signal, and a the board is ready to process a new event.

Default value = 50.

23 (0x2E) – buildn_reg (r/o)

Build identification number: should change when changes are introduced to the FW.

## One-wire lines operation

Each one of the two 1-wire lines present is controlled by a set of three registers: registers 2-4 for the 1.2 V monitor, registers 5-7 for the 3.3 V monitor.

Writing the ctrl_reg starts the command identified by the firtst ‘1’ bit (starting by the lsb).

- Init: the initialization pulse is asserted.

- Write 8b (byte-level write): writes to the 1-wire line the byte previously written at register data_reg.

- Write 1b (bit-level write): writes to the 1-wire line the LSB of the byte previously written at register data_reg. Note that the LSB bit is sent every time the command is asserted: thus, writing a byte at data_reg and issuing 8 times a bit-level write command is not equivalent to issuing one byte-level write command.

- Read 8b (byte-level read): reads a byte from the 1-wire line. The result is stored at data_reg and the calculated CRC is stored at crc_reg (after the communication of a complete frame with the CRC information, the CRC register should be “00000000”). As specified in the 1-wire protocol, the LSB is the first to be communicated.

- Read 1b (bit-level read): reads a bit from the 1-wire line, which can be read at the MSB of data_reg. Every time a bit is read, the data_reg register shifts one bit to the right, the old LSB is lost and the newly read bit becomes the MSB. The crc_reg is updated accordingly. Note that this implies that issuing 8 times a bit-level read operation is equivalent to issuing a byte-level read operation.

## Optical modules control and monitoring

The signal detect outputs from all four optical receivers are continuously monitored and mirrored in the 4 lower bits of register sd_status_reg. These same four signals are latched onto the 4 higher bits of this same register, so that a temporary loss of signal doesn’t go undetected. Issuing a write command on this register clears the latches. The four receivers are:

- sd_avago1: the combined SD for all channels in the top  avago receiver (ch. 0-11)

- sd_avago2: the combined SD for all channels in the bottom avago receiver (ch. 12-23)

- sd_tsc: the receiver part of the top finisar transceiver module, that carries the TSC serial link

- sd_ch24:  the receiver part of the bottom finisar transceiver module, that carries 24th channel from the minicrates

The control bits in register opto_ctrl_reg are mirrored to the lines going to the optical modules. The signals are as follow:

- tx1_dis and tx2_dis: transmitter disable control signals for the transmitter part of the two finisar transceiver modules. The top transmitter is tx2 and the bottom transmitter is tx1.

- Each avago (1-top, 2-bottom) has 3 control signals: signal detect enable, receiver enable and squelch enable.

The default value for this register is “11111111” (transmitters disabled and reception, squelch and SD enabled on the avago modules).

## TSC link

### Overview

Before the DTE upgrade there’s a communication between each sector’s ROS and TSC board, which are adjacent to each other in the crate, carried through the TIMbus backplane. After the upgrade, ROS and TSC board are no longer in the same crate and this is information is transmitted by means of two intermediate boards, the TSC_rear, a RTM for TSC, and the OFCu-RO, a RTM for the ROS, and a serial optical fibre link. This communication is essentially unidirectional from the TSC to the ROS.

The TSC_rear plugs to the backplane of the TSC crate and communicates with a TSC board through the pass-through connector in it. It emulates the behaviour of an adjacent ROS board, signaling the ready status and receiving the 16-bit parallel bus data from the TSC. It adds a layer of communication to transmit metadata such us the event number or the word count, or the detection of an event counter reset. The information is transmitted forming 20-bit serial words, with a start and stop bit, a valid bit, a word-type bit, and 16 payload data bits in each LHC clock cycle. Thus, the data rate of the serial link is 800 Mbps.

The OFCu-RO receives this link and deserializes it synchronously using the same LHC clock. It checks that the data received is compliant with the established protocol, and, if no errors are found, it delivers the data to the ROS board to which it is connected through the pass through connector in the backplane, mimicking the behaviour of the no-longer-adjacent TSC board.

### OFCu-RO-specific information

When the FPGA boots, it initializes the internal pll for clock generation, the phase detector and input delay for correct eye-center sampling, and the input deserializer and word alignment logic. When an idle word is received it is immediately discarded, and any non-idle word (except for the special case of the ECR word) is written into a FIFO for later availability.

After boot the FPGA is ready for data reception, but almost any error would send it immediately to the error state in which incoming information is discarded and no data is delivered to the ROS (however, if ros_ready is asserted while in error state, a simple handshake is carried over with a dummy word to prevent the ros from waiting the tsc data timeout). This is done to prevent incorrect or unaligned data delivery. There’s a FW hard-coded mask that currently only allows err_stayatlimit flag to be bypassed. The only way out of this state is by the reception of an ECR signal, which resets the event counter and clears the error flag registers. The ECR cycle is completed if and only if a ECR word is received through the serial link before a timeout, to indicate that the ECR, which is an LHC global signal, has also been correctly received and processed at the TSC_rear. For debug purposes, a successfully completed ECR cycle can be forced by issuing a write command on register tsc_status_0_la.

When a L1A trigger is received it is queued in order to process when it is possible. Whenever the FPGA is in the idle state and the presence of a queued L1A trigger is detected, a data frame delivery cycle is started: the ros_ready signal is asserted by ROS, the event number coincidence between the header word and the local counter is verified, and as soon as payload data is available it is delivered to the ROS by writing it in the 16-bit parallel bus and asserting the trg_strobe signal. For as long as there is new data and ros_ready flag is active the communication continues, and when data ends, the number of words counted is compared with the counter on the trailer word, trg_strobe is de-asserted and the ROS consequently de-asserts the ros_ready signal. If no errors have occurred the system goes back to the idle state.

Registers tsc_maxwords, tsc_ecrwait, tsc_roswait1, tsc_headerwait, tsc_datawait and tsc_roswait2 correspond to different parameters and limits of the optical link to ros logic.

## LED indicators

There are 6 programmable LED in the OFCu-RO board, four of which are visible from the front panel by means of a light guide. These four LEDs serve a dual purpose:

- Right after FPGA boot or reset the four LEDs are switched on sequentially during several seconds to indicate a successful load of the FW and presence of a working clock. The cycle lasts (+) seconds approximately with each LED being on for (+) ms approximately.

- After this, they serve as indicators:

  - SD: continuous green if all four signal detect lines are asserted. If any of the four SD lines is low, the LED repeatedly flashes four times: one for each receiver module. A long flash indicates that the corresponding SD signal is high, whereas a short flash indicates a low SD.

  - CTRL: flashes intermittently when registers are being accessed through the slow control interface.

  - TSC:  continuous green if TSC link is locked, intermittent if it’s locking and unlocking, off if unlocked.

  - TTC: short flash indicates L1A, long flash ECR.

# Test-specific information

The FW for the OFCu-RO and TSC_rear boards is generated from the same code, changing some parameters that determine which modules are compiled and which ones are excluded. Also, two types of builds exist for the OFCu board: validation and operation, each used for different phases of the deployment (validation of the prototypes, production test to verify correct manufacture of each board, and operation for the final system).

This section describes some particularities of each build, which is useful for the validation and production phases.

## Modifications by functional block

### Optical modules signals in TSC_rear builds

opto_ctrl_reg in the TSC_rear board controls the same signals as it does in the controls same things, although they are unconnected. In particular, the tx1_dis signal is used during test.

opto_ctrl_reg also controls the value of the sd_ch24 (bit 2), sd_avago2 (bit 1) and sd_avago1 (bit 0), which in the TSC_rear act as outputs, since there’s actually no physical optical module present. Thus, this register can be used to validate the PCB manufacture without actually changing the optical signals in the receivers. The sd_status_reg bits, in this configuration, reflect the behaviour of these user-controlled signals.

### TSC link recent history data in OFCu-RO builds

In order to be able to debug the functioning of the TSC link interface logic to the ROS board, there is a memory element that stores the recently received words (depth can be configured by changing FW). The data width is 1 byte to ease register-based readout, and thus each incoming word has to be written using 3 bytes (remaining bits are used for other purposes; see FW). A brief summary is given here; in order to know the details, the code should be inspected.

- During normal operation, the memory is shifted 3 bytes (and the 3 oldest ones are discarded) and new information is inserted if:

  - If the L1A signal is high, three bytes are shifted in to mark the event. A received word may be lost and not registered.

  - If the word is not idle, it is registered.

- If an error is detected, some more words are still registered and then recording stops.

- Writing in register tsc_status_0_la (successful ECR simulation) restarts recording, as does writing in register test1_reg (when the tsc-link receiver state machine is returned to operation by a real, not simulated, successful ECR, the recording is not automatically restarted).

- Reading in test0_reg returns the last shifted word, and writing in this register shifts back the entire memory 1 byte (readout of the memory acts as a LIFO, whereas recording functions as a FIFO).

### Deserializer’s iodelay2 tap value

In the OFCu builds a value is written to register test1_reg that serves to identify the status of the deserializer’s iodelay2 tap status: after reset (deserializer reset occurs at global reset, on bufpll unlock and on a tsc_status_2_la write operation) it starts at 128 (0x80) and increments/decrements every time DLY_CE is asserted (which happens automatically if the phase detector indicates need for it). The relationship of this count with the actual delay value for the master and slave iodelay2 depends on the history and the initial phase relationship: The master is configured to stay_at_limit while the slave is configured to wraparound, so for certain evolution of the phase relationship the difference between the two of them may separate from the ideal value of half a bit (for the frequencies in use, 1 bit ~ 45 taps). Also, every approximately 5 seconds a CAL order is issued to the slave iodelay2, so this relationship is restored.

### Serializer

The serializer module is present in the TSC_rear builds and also in the validation build of the OFCu-RO, where it is used to verify the proper functioning of block.

The following table summarizes the different configurations:

| Build type | Serializer present? | Serializer input from module… | Tx1 | Tx2 |
| --- | --- | --- | --- | --- |
| OFCu-RO, validation | YES | test | 0 | Serializer |
| OFCu-RO, operation | NO | --- | 0 | 0 |
| TSC_rear | YES | Tscj3 | 0 | Serializer |

### Test module

In the validation build (and, therefore, only for the OFCu board) the test module carries out the following tasks:

- The output word, which serves as the serializer input, is selected by ow1_ctrl_reg(7 downto 6).

  - 00 pseudorandom: The output word has start and stop bit, and the 18 “payload” bits are selected from a 360-bits-long pseudorandom string (which is cycled every 20 clock edges).

  - 01 idle: all words are idle (10 zeros, 10 ones)

  - else clk400: out of every 20 words, one corresponds to an idle word (to make it possible for the serializer to find the start and stop bits) and the rest correspond to ones and zeroes alternating.

- An state machine locks to the input word (received from the deserializer) and aligns it to the data pattern that is being sent. If an error is detected, a 6 bit counter (test2_reg(5 downto 0) is incremented. Note that in case lock is lost either in the deserializer or here, the error counter does not increase.

- Test2_reg(7 downto 6) reflect the real time values of signals read_mode or bspare(0)

- Test2_reg resets on test2_reg write

- testout(20) is controlled by ow1_write_reg:

  - 000xxxxx: deserialized word’s bit # determined by ow1_write_reg’s 4 lsb

  - other: clk20

- In the remaining testouts, clk20 is driven

In the operation build the test module carries out the following tasks:

- The even pins in testconn(20 downto 1) drive a clk20 signal, and is expected to be read at all the odd pins. Otherwise, an error flag is set at test2_reg(0), with a latch in test2_reg(1)

- Test2_reg(7 downto 6) reflect the real time values of signals read_mode or bspare(0)

## Register description

|  | register value function | WRITE |
| --- | --- | --- |
|  | Validation | Operation | Validation | Operation |
| 0 (0x00) moregs_data | Buffer register for extended register space access | Write register |
| 1 (0x02) moregs_ctrl | Control register for extended register space | Write register and issue command |
| 2 (0x04) ow1_ctrl | +select serial pattern | 1.2V 1-wire control | Write register and issue command |
| 3 (0x06) ow1_data | +select testconn(1) driver | 1.2V 1-wire write byte | Write register |
| 4 (0x08) ow1_crc | 1.2V 1-wire crc byte |  |
| 5 (0x0A) ow3_ctrl | 3.3V 1-wire control, build type identification | Write register and issue command, write build type in 3 MSB |
| 6 (0x0C) ow3_data | 3.3V 1-wire data byte | Write register |
| 7 (0x0E) ow3_crc | 3.3V 1-wire crc byte |  |
| 8 (0x10) sd_status | Live and latched receivers’ SD values. | Reset sd_status_reg’ latches. |
| 9 (0x12) opto_ctrl | Avago rx’ and finisar tx’ control outputs TSC_rear only: drives SDs | Write register |
| 10 (0x14) tsc_status0 | TSC link error flags (latched) | Simulate ECR |
| 11 (0x16) tsc_status1 | TSC link error flags (latched) | Reset tsc_statusX_reg |
| 12 (0x18) tsc_status2 | TSC link error flags (latched) | Reset deserializer |
| 13 (0x1A) test0_reg | OFCu-RO: Tsc link debug memory top byte | OFCu-RO: Shift 1 byte the tsc link debug memory |
| 14 (0x1C) test1_reg | Deser delay tap indicator | OFCu-RO: Restart recording in tsc link debug memory |
| 15 (0x1E) test2_reg | Serial loopback test, spare lines latch | Testconn loopback test, spare lines latch | reset test2_reg |
| 16 (0x20) tsc_maxwords | Maximum TSC-ROS event size | Write register |
| 17 (0x22) tsc_strobewait | Maximum wait cycles for assertion of trg_strobe | Write register |
| 18 (0x24) tsc_ecrwait | Maximum wait cycles for arrival of ECR word through serial link | Write register |
| 19 (0x26) tsc_roswait1 | Maximum wait cycles for assertion of ros_ready signal ( / 64) | Write register |
| 20 (0x28) tsc_headerwait | Maximum wait cycles for arrival of header word through serial link | Write register |
| 21 (0x2A) tsc_datawait | Maximum wait cycles for arrival of first data word through serial link | Write register |
| 22 (0x2C) tsc_roswait2 | Maximum wait cycles for de-assertion of signal ros_ready | Write register |
| 23 (0x2E) buildn_reg | Build identification number |  |

Note: “+xxxx” indicates a functionality added to the base operation build.