VME_PATCH

User Manual

Version 3.0

C. Fernández Bedoya, A. Navarro Tobar, J. Sastre Álvaro

CIEMAT

October 30th, 2013

.

INDEX

1	VME_PATCH BOARD	5

2	VME_PATCH INTERFACES	6

3	VME_PATCH ADDRESSING	7

4	VME_PATCH BOARD REGISTERS	8

5	ACCESSING THE CUOF MEZZANINE	11

# VME_PATCH BOARD

The goal of this board is to perform the bridge between the VME controller of the ROS and TSC crates (usually Linco VME controller) and the OFCU and TSC_rear modules.

Figure 1: Front image of the VME_PATCH board.

Figure 2: Back image of the VME_PATCH board.

Figure 3: Image of the VME_PATCH front pannel

# VME_PATCH INTERFACES

The front panel has:

- DA-15 male connector that contains four I2C buses with the following mapping:

Figure 4: I2C DA-15 P  male connector

Note that the corresponding DA-15 female socket must have the pin-out mirrored:

Figure 5: I2C DA-15 S  female socket

- First row of leds. From left to right:

  - ON = 1.2 V ok [D5 = 1.2 V]

  - ON = 3.3 V ok [D6 = 3.5 V]

- Second row of leds. From left to right:

  - ON = All signal detects of the OFCU boards in the crate are OK [D1 = SD OK]

  - ON = VME access data acknowledge of the VME_patch [D3 = DTACK]

  - ON = VME_patch FPGA properly programmed (done) [D4 = DONE]

The backplane connections contain a J1 VME standard connector and a custom J2 to connect to the J2_OFCU backplane. The J2 mapping is (the signals in grey do not exist at present):

Figure 6: J2 VME_patch mapping

The schematics of the VME_PATCH board can be found here:

http://wwwae.ciemat.es/cms/DTE/iupgrade.htm#VMEpatch

# VME_PATCH ADDRESSING

The VME_PATCH board supports short non-privileged A16 D16 (Word) VME access. It translates it to the OFCU boards by means of a custom parallel protocol.

The A16 base address is selected with switch SW13, (A15-A10).

The address mapping for the registers of the different functional blocks is what follows:

| A16 Base Address (A15 – A10) | Functional block |
| --- | --- |
| VME_PATCH + 0x00 a 0x3E | VME_PATCH |
| VME_PATCH + 0x40 a 0x5E | OFCU slot 1 |
| VME_PATCH + 0x80 a 0x9E | OFCU slot 2 |
| VME_PATCH + 0xC0 a 0xDE | OFCU slot 3 |
| VME_PATCH + 0x100 a 0x11E | OFCU slot 4 |
| VME_PATCH + 0x140 a 0x15E | OFCU slot 5 |
| VME_PATCH + 0x180 a 0x19E | OFCU slot 6 |
| VME_PATCH + 0x1C0 a 0x1DE | OFCU slot 7 |
| VME_PATCH + 0x200 a 0x21E | OFCU slot 8 |
| VME_PATCH + 0x240 a 0x25E | OFCU slot 9 |
| VME_PATCH + 0x280 a 0x29E | OFCU slot 10 |
| VME_PATCH + 0x2C0 a 0x2DE | OFCU slot 11 |
| VME_PATCH + 0x300 a 0x31E | OFCU slot 12 |

| 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | J2_3 | J2_2 | J2_1 | J2_0 |  |  |  |  |  | Vme BYTE |

# VME_PATCH BOARD REGISTERS

#### Reg1_vme (VME_PATCH + 0x00)

Default value = 0x0

Reset by a local_reset.

| Bits | description | acc |  |
| --- | --- | --- | --- |
| 0-2 | Dummy | R/W |  |
| 3 | Lights SD LED | R/W | Turns on the SD led in the front panel of the VME_patch even if the SD signals are not correct |
| 4 | Read _J2 | R/W | Sets the line Read_J2 |
| 5 | Spare _J2 | R/W | Sets the line Spare _J2 |
| 6 | OFCU Reset | W | =1 reset (100 ns pulse). A reset will be sent sequentially to each OFCU. |
| 7 | Local_reset | W | =1 reset of the VME_PATCH board only |

All the registers from VME_PATCH are reset by a local reset.

A VME sys-reset will force also a reset in the VME_PATCH and in the OFCU boards.

#### Interruptions_Set (VME_PATCH + 0x02)

Default value = 0x0

Reset by a local_reset.

| Bits | description | acc |  |
| --- | --- | --- | --- |
| 0 | enable test interrupt | R/W | = 1 an interruption will be generated |
| 1 | interrupt requested | R | = 1 an interruption from the VME_PATCH has occurred. |
| 2-7 | Dummy | R/W |  |

#### Interruptions_Vector (VME_PATCH + 0x04)

Default = 0x0

Reset by a local_reset.

| Bits | Description | acc |  |
| --- | --- | --- | --- |
| 0-7 | interrupt vector | R/W |  |

Interrupt Level is always 7

#### SCL (VME_PATCH + 0x06)

Default = 0x1

Reset by a local_reset.

| Bits | Description | acc |  |
| --- | --- | --- | --- |
| 0 | SCL write | W | SCL signal. The I2C bus you are addressing is selected in register I2C select. |
| 1 | SCL read | R | SCL signal registered each clock cycle. The I2C bus you are addressing is selected in register I2C select (0x0A) |
| 2-7 | ‘0’ | - |  |

#### SDA (VME_PATCH + 0x08)

Default = 0x1

Reset by a local_reset.

| Bits | Description | acc |  |
| --- | --- | --- | --- |
| 0 | SDA write | W | SDA signal. The I2C bus you are addressing is selected in register I2C select (0x0A) |
| 1 | SDA read | R | SDA signal registered each clock cycle. The I2C bus you are addressing is selected in register I2C select (0x0A) |
| 2-7 | ‘0’ | - |  |

#### I2C SELECT (VME_PATCH + 0x0A)

Default = 0x0

Reset by a local_reset.

| Bits | Description | acc |  |
| --- | --- | --- | --- |
| 0 | A0 – selection of I2C bus to address | R/W |  |
| 1-3 | - | - |  |
| 4 | A1 – selection of I2C bus to address | R/W |  |
| 5-7 |  | - |  |

0x00 => SDA0, SCL0

0x01 => SDA1, SCL1

0x10 => SDA2, SCL2

0x11 => SDA3, SCL3

#### SIGNAL DETECT OFCU 1-2 (VME_PATCH + 0x0C)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=1, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=1, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=1, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=2, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=2, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=2, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

SIGNAL DETECT

= 1 MEANS ALL OK (OFCU board connected, Avagos in, signal received)

=0 MEANS THERE IS A CHANNEL THAT IS IN NOT RECIVING SIGNAL

#### SIGNAL DETECT OFCU 3-4 (VME_PATCH + 0x0E)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=3, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=3, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=3, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=4, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=4, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=4, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

#### SIGNAL DETECT OFCU 5-6 (VME_PATCH + 0x10)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=5, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=5, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=5, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=6, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=6, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=6, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

#### SIGNAL DETECT OFCU 7-8 (VME_PATCH + 0x12)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=7, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=7, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=7, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=8, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=8, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=8, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

#### SIGNAL DETECT OFCU 9-10 (VME_PATCH + 0x14)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=9, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=9, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=9, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=10, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=10, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=10, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

#### SIGNAL DETECT OFCU 11-12 (VME_PATCH + 0x16)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0 | Signal Detect OFCU=11, ROS ch 0-11 MB1and MB2 | R |
| 1 | Signal Detect OFCU=11, ROS ch 12-23 MB3and MB4 | R |
| 2 | Signal Detect OFCU=11, ROS ch 24 (single) MB4-b last | R |
| 3 | Signal Detect OFCU=12, ROS ch 0-11 MB1and MB2 | R |
| 4 | Signal Detect OFCU=12, ROS ch 12-23 MB3and MB4 | R |
| 5 | Signal Detect OFCU=12, ROS ch 24 (single) MB4-b last | R |
| 6-7 | - |  |

#### OFCU_RESET (VME_PATCH + 0x18)

Default = 0x0

Reset by a local_reset.

| bits | Description | acc |
| --- | --- | --- |
| 0-7 | OFCU Slot to which a reset wants to be issued (75 ns reset pulse) | R/W |

The number you write here is the OFCU slot (i.e. sector) to which a reset will be sent. 0x1 to reset OFCU from sector 1, 0x5 to reset OFCU sector 5, etc.

# ACCESSING THE CUOF MEZZANINE

The VME_PATCH board can be used to access the CUOF mezzanine for configuration through the DA-15 connector in the front of the board.

You need to connect a cable like the one in the picture to each of the individual pseudo-I2C channels. Alternatively, you can make an OR of all the lines from the 8 laser drivers in the CUOF mezzanine and access all of them simultaneously (clearly, the same bias/modulation parameters will be configured for all of the laser drivers).

Writing in the I2C_SELECT register of the VME_PATCH you can choose which of the 4th channels is going to be used for the I2C transmission. In addition writing in the SDA and SCL registers, you can send the appropriate commands. An example of the software to be used can be found here:

http://wwwae.ciemat.es/cms/DTE/iupgrade.htm#VMEpatch