REGISTROS ROSTEST

Acceso Word (D16), A16 non-priviledged data access. Board addressing space 0x1000.

CAMBIOS EN EL DISEÑO

Entradas y salidas:

Para este diseño he considerado que en la tarjeta se podían añadir las siguientes entradas y salidas:

5 entradas

4 LVDS: pulse0_in, pulse1_in y L1A_lvds_in, clock_lvds.

1 NIM: L1A_nim_in

4 salidas:

3 LVDS: pulse0_out, pulse1_out, autoL1A

1 NIM: L1A_nim_out

Relojes:

- Timclk (del conector del timbus, el que ya está puesto)

- Ckdesv2 (cogerlo también del conector del timbus y pasarlo a TTL, recordar que es una señal común al bus).

- Clk_cristal: poner un cristal de 40 MHz.

- Clk_externo: para usar un reloj externo de frecuencia distinta al resto. Yo creo que puede ser entrada lvds y convertirlo a TTL en la tarjeta.

Direcciones:

He incluido una memoria de 1024 words D16 para probar a mandar datos a la FIFO del sector collector de la ROS (y poder conseguir un FIFO full). He mapeado el espacio de direcciones de forma que:

$00 a $800: espacio de registros

$800 a $FFF: espacio de memoria.

Por tanto a la FPGA le tienen que entrar las líneas de la tarjeta de A10 a A0, y en el switch y comparador de dirección base de la tarjeta hay que dejar sólo VA14 a VA11.

Varios:

- Creo que ya sabías que faltaban las Resistencias de terminación de ROSready y de timclk.

- Faltaba por sacar la señal AutoL1A al conector del TIMbackplane.

- Faltaría por coger ckdesv2 del TIMbackplane.

- Poner un led para el done de la FPGA.

- Los pull-ups y pull-downs de IN1+/- del U14 y de OFF0+/- y OFF1+/-, no están al revés para que salga un 0?

ROB-ROS INTERFACE

Channel enable Low $00

| 0-15 | Enable channel | R/W | =1 => enabled |
| --- | --- | --- | --- |

Channel enable High $02

| 0-8 | Enable channel | R/W | =1 => enabled |
| --- | --- | --- | --- |

CONTROL

Control & status $04

| 0-1 | Select board clock (except pulses) | R/W | 0=> timclk, 1=> ck_desv2, 2=> crystal, 3 => external (lvds) |
| --- | --- | --- | --- |
| 1 | Max number of triggers done | R |  |
| 15 | Reset | W |  |

Pulse0_out and Pulse1_out Register $06

| 0 | PULSE 0: Select pulse 0 input (lvds) | R/W |  |
| --- | --- | --- | --- |
| 1 | PULSE 0: Select pulse 1 input (lvds) | R/W |  |
| 2 | PULSE 0: Select trigger_internal | R/W |  |
| 3 | PULSE 0: Select trigger_internal_delayed | R/W |  |
| 4-5 | Synchronize to clock | R/W | 0=> internal, 1 => tim_clk 2=> ckdesv2 |
| 6 | PULSE 1: Select pulse 0 input (lvds) | R/W |  |
| 7 | PULSE 1: Select pulse 1 input (lvds) | R/W |  |
| 8 | PULSE 1: Select trigger_internal | R/W |  |
| 9 | PULSE 1: Select trigger_internal_delayed | R/W |  |
| 10-11 | Synchronize to clock |  | 0=> internal, 1 => tim_clk, 2=> ckdesv2 |

Trigger_internal, L1A_nim_out, Auto_L1A_output Register $08

| 0 | INTERNAL_TRIGGER: Enable L1A_lvds_in | R/W |  |
| --- | --- | --- | --- |
| 1 | INTERNAL_TRIGGER: Enable L1A_nim_in | R/W |  |
| 2 | INTERNAL_TRIGGER: Enable AutoL1A | R/W |  |
| 3 | INTERNAL_TRIGGER: Enable random generation | R/W |  |
| 4-7 | Average random Frequency selection | R/W | Rand_freq |
| 8 | L1A_nim_out: Select trigger_internal | R/W |  |
| 9 | L1A_nim_out: Select trigger_internal_delayed | R/W |  |
| 10 | AUTOL1A output: Select trigger_internal | R/W |  |
| 11 | AUTOL1A output: Select trigger_internal_delayed | R/W |  |

Random frequency: (If the input clock is 40 MHz, otherwise, 15 => clock_freq/2 and consecutive /2 for the following values).

0	610 Hz

1	1,22 kHz

2	2,44 KHz

3	4,88 KHz

4	9,76 KHz

5	19,53 KHz

6	39, 06 KHz

7	78,125 KHz

8	156,25 KHz

9	312,5 KHz

10	625 kHz

11	1,25 MHz

12	2,5 MHz

13	5 MHz

14	10 MHz

15	20 MHz

VME generation Register $0A

| 0 | Generate trigger_internal | W |  |
| --- | --- | --- | --- |
| 1 | Generate pulse_0 | W |  |
| 2 | Generate pulse_1 | W |  |
| 3 | Generate autoL1A | W |  |

Programmable Trigger internal delay $0C

| 0 - 15 | Delay register for the trigger (steps of 100 ns) | R/W |  |
| --- | --- | --- | --- |

It is a shift register driven with a 100 ns clock. You just write a 1 in the bit of the desired delay.

Bit 0: 100 ns

Bit 1: 200 ns

Bit 2 300 ns

Etc.

Max number trigger $0E

| 0-15 | Maximum number of triggers to send | R/W | 0 => no limit |
| --- | --- | --- | --- |

Number of triggers sent $10

| 0-15 | Trigger counter | R/W |  |
| --- | --- | --- | --- |

(Se resetea el contador de triggeres automáticamente cuando vuelves a escribir el máximo número de triggeres que quieres enviar. Se incrementa con cualquier trigger que llegue de cualquier sitio y esté habilitado.)

SECTOR COLLECTOR INTERFACE

Time wait for trigger strobe after ROS ready $12

| 0-11 | Number of bunch cycles to wait | R/W | Trg_str_delay |
| --- | --- | --- | --- |
| 12 | Disable answer to ROS ready | R/W | Dis_trg_str |

Max number of words to send $14

| 0-15 | Max number of words to send | R/W |  |
| --- | --- | --- | --- |

Dummy $16

| 0-15 | Dummy register | R/W |  |
| --- | --- | --- | --- |

Sector Collector Memory $800 - $FFF

| 0-15 | Data | W |  |
| --- | --- | --- | --- |

La dirección base de la tarjeta se elije con A15 alA12.

La tarjeta necesita un espacio de 0x1000 direcciones, de Base address a Base address+0xFFF.

PINLOCK

#Sun Apr 09 15:25:01 2006

| Pin Number | Signal Name | Pin Usage | Pin Name |
| --- | --- | --- | --- |
| P1 |  |  | GND |
| P2 |  |  | TMS |
| P3 |  | IOB |  |
| P4 |  | IOB |  |
| P5 |  | IOB |  |
| P6 | done_in | IOB | IO_VREF_7 |
| P7 | done_out | IOB |  |
| P8 |  | IOB |  |
| P9 |  | IOB |  |
| P10 |  | IOB |  |
| P11 |  |  | GND |
| P12 |  |  | VCCO |
| P13 |  |  | VCCINT |
| P14 |  | IOB |  |
| P15 |  | IOB |  |
| P16 | trg_data<4> | IOB |  |
| P17 | auto_L1A_p | IOB |  |
| P18 | tp4 | IOB |  |
| P19 |  |  | GND |
| P20 | sel_rob<4> | IOB | IO_VREF_7 |
| P21 | trg_data<5> | IOB |  |
| P22 | trig_out_p | IOB |  |
| P23 | trg_data<7> | IOB |  |
| P24 | trg_data<6> | IOB | IO_IRDY |
| P25 |  |  | GND |
| P26 |  |  | VCCO |
| P27 | sel_rob<18> | IOB | IO_TRDY |
| P28 |  |  | VCCINT |
| P29 | sel_rob<16> | IOB |  |
| P30 | trg_data<8> | IOB |  |
| P31 | sel_rob<1> | IOB | IO_VREF_6 |
| P32 |  |  | GND |
| P33 | trg_data<11> | IOB |  |
| P34 | trg_data<3> | IOB |  |
| P35 | L1A_lvds_in | IOB |  |
| P36 | trg_data<0> | IOB |  |
| P37 | trg_data<1> | IOB |  |
| P38 |  |  | VCCINT |
| P39 |  |  | VCCO |
| P40 |  |  | GND |
| P41 | trg_data<2> | IOB |  |
| P42 | sel_rob<15> | IOB |  |
| P43 | L1A_nim_in | IOB |  |
| P44 | tp3 | IOB |  |
| P45 | on245 | IOB | IO_VREF_6 |
| P46 | trg_data<10> | IOB |  |
| P47 | trg_data<9> | IOB |  |
| P48 | tp2 | IOB |  |
| P49 | tp1 | IOB |  |
| P50 |  |  | M1 |
| P51 |  |  | GND |
| P52 |  |  | M0 |
| P53 |  |  | VCCO |
| P54 |  |  | M2 |
| P55 |  |  | NC |
| P56 |  |  | NC |
| P57 | g245 | IOB |  |
| P58 | dtack | IOB |  |
| P59 | trg_data<12> | IOB | IO_VREF_5 |
| P60 | trg_data<13> | IOB |  |
| P61 | trg_data<14> | IOB |  |
| P62 | trg_data<15> | IOB |  |
| P63 | db<8> | IOB |  |
| P64 |  |  | GND |
| P65 |  |  | VCCO |
| P66 |  |  | VCCINT |
| P67 | db<3> | IOB |  |
| P68 | db<4> | IOB |  |
| P69 | db<5> | IOB |  |
| P70 | db<15> | IOB |  |
| P71 | write | IOB |  |
| P72 |  |  | GND |
| P73 | db<0> | IOB | IO_VREF_5 |
| P74 | w245 | IOB |  |
| P75 | db<12> | IOB |  |
| P76 |  |  | VCCINT |
| P77 | ckdesv2_p | GCLKIOB | GCK1 |
| P78 |  |  | VCCO |
| P79 |  |  | GND |
| P80 | clk_ext_p | GCLKIOB | GCK0 |
| P81 | db<13> | IOB |  |
| P82 | brd_sel | IOB |  |
| P83 | db<14> | IOB |  |
| P84 | db<11> | IOB | IO_VREF_4 |
| P85 |  |  | GND |
| P86 | db<2> | IOB |  |
| P87 | am0 | IOB |  |
| P88 | db<9> | IOB |  |
| P89 | db<7> | IOB |  |
| P90 | db<6> | IOB |  |
| P91 |  |  | VCCINT |
| P92 |  |  | VCCO |
| P93 |  |  | GND |
| P94 | lword | IOB |  |
| P95 | am1 | IOB |  |
| P96 | am5 | IOB |  |
| P97 | am4 | IOB |  |
| P98 | am3 | IOB | IO_VREF_4 |
| P99 | iack | IOB |  |
| P100 | add_in<0> | IOB |  |
| P101 |  | IOB |  |
| P102 |  | IOB |  |
| P103 |  |  | GND |
| P104 |  |  | DONE |
| P105 |  |  | VCCO |
| P106 |  |  | PROGRAM |
| P107 |  | IOB | IO_INIT |
| P108 |  | IOB | IO_D7 |
| P109 |  | IOB |  |
| P110 |  | IOB |  |
| P111 | ds1 | IOB | IO_VREF_3 |
| P112 | ds0 | IOB |  |
| P113 |  | IOB |  |
| P114 | as | IOB |  |
| P115 | add_in<2> | IOB | IO_D6 |
| P116 |  |  | GND |
| P117 |  |  | VCCO |
| P118 |  |  | VCCINT |
| P119 | add_in<5> | IOB | IO_D5 |
| P120 | add_in<6> | IOB |  |
| P121 | add_in<10> | IOB |  |
| P122 |  | IOB |  |
| P123 | add_in<9> | IOB |  |
| P124 |  |  | GND |
| P125 |  | IOB | IO_VREF_3 |
| P126 | add_in<4> | IOB | IO_D4 |
| P127 | add_in<8> | IOB |  |
| P128 |  |  | VCCINT |
| P129 | sel_rob<19> | IOB | IO_TRDY |
| P130 |  |  | VCCO |
| P131 |  |  | GND |
| P132 | add_in<7> | IOB | IO_IRDY |
| P133 | sel_rob<3> | IOB |  |
| P134 | sel_rob<23> | IOB |  |
| P135 | pulse_1_out | IOB | IO_D3 |
| P136 | sel_rob<7> | IOB | IO_VREF_2 |
| P137 |  |  | GND |
| P138 | sel_rob<6> | IOB |  |
| P139 |  | IOB |  |
| P140 | pulse_0_out | IOB |  |
| P141 |  | IOB |  |
| P142 |  | IOB | IO_D2 |
| P143 |  |  | VCCINT |
| P144 |  |  | VCCO |
| P145 |  |  | GND |
| P146 |  | IOB | IO_D1 |
| P147 |  | IOB |  |
| P148 |  | IOB |  |
| P149 |  | IOB |  |
| P150 |  | IOB | IO_VREF_2 |
| P151 |  | IOB |  |
| P152 |  | IOB |  |
| P153 | iackin | IOB | IO_DIN_D0 |
| P154 | iackout | IOB | IO_DOUT_BUSY |
| P155 |  |  | CCLK |
| P156 |  |  | VCCO |
| P157 |  |  | TDO |
| P158 |  |  | GND |
| P159 |  |  | TDI |
| P160 |  | IOB | IO_CS |
| P161 |  | IOB | IO_WRITE |
| P162 |  | IOB |  |
| P163 |  | IOB |  |
| P164 |  | IOB | IO_VREF_1 |
| P165 |  | IOB |  |
| P166 | sel_rob<21> | IOB |  |
| P167 | trg_strobe | IOB |  |
| P168 | ros_ready | IOB |  |
| P169 |  |  | GND |
| P170 |  |  | VCCO |
| P171 |  |  | VCCINT |
| P172 | sel_rob<5> | IOB |  |
| P173 | sel_rob<0> | IOB |  |
| P174 | sel_rob<24> | IOB |  |
| P175 | sel_rob<9> | IOB |  |
| P176 | sel_rob<8> | IOB |  |
| P177 |  |  | GND |
| P178 | add_in<3> | IOB | IO_VREF_1 |
| P179 | add_in<1> | IOB |  |
| P180 | sel_rob<11> | IOB |  |
| P181 | db<1> | IOB |  |
| P182 | timclk_p | GCLKIOB | GCK2 |
| P183 |  |  | GND |
| P184 |  |  | VCCO |
| P185 | clk_cristal_p | GCLKIOB | GCK3 |
| P186 |  |  | VCCINT |
| P187 | db<10> | IOB |  |
| P188 | sel_rob<10> | IOB |  |
| P189 | sel_rob<12> | IOB | IO_VREF_0 |
| P190 |  |  | GND |
| P191 | sel_rob<13> | IOB |  |
| P192 | sel_rob<14> | IOB |  |
| P193 | sel_rob<2> | IOB |  |
| P194 | sel_rob<17> | IOB |  |
| P195 | pulse_1_lvds | IOB |  |
| P196 |  |  | VCCINT |
| P197 |  |  | VCCO |
| P198 |  |  | GND |
| P199 | sel_rob<20> | IOB |  |
| P200 | sysreset | IOB |  |
| P201 | sel_rob<22> | IOB |  |
| P202 | pulse_0_lvds | IOB |  |
| P203 |  | IOB | IO_VREF_0 |
| P204 |  | IOB |  |
| P205 |  | IOB |  |
| P206 |  | IOB |  |
| P207 |  |  | TCK |
| P208 |  |  | VCCO |